## Slide 1: Husqvarna Research Platform

## Slide 2
What is the Husqvarna Research Platform?
ROS enabled durable outdoor robot
  Operates in all weathers
  Operates 24/7 with automatic charging
  Includes Gazebo models for simulated environment
  Simple ros interface via provided driver (velocity in, odometry out)
  Add your own computing platform and sensors depending on research

## Slide 3: Standard Automower 330X
Bumper (collision) with all directions of chassis. Will also detect “lift” for safety reasons.
Pivoting wheels (2) + 2 rear wheels
Wire sensors Bad at distance but very good close to wire.

## Slide 4: Standard Automower 330X
Main board (STM32-based)
GUI board (STM32-based) Includes buttons/display
Wire Sensor
Wire Sensor
Wire Sensor
Collision Sensor
Collision Sensor
Accel
Wheel Motor
Wheel Motor
Encoder
Encoder
”Standard Mower SW”
GPS
Battery

## Slide 5: Research Automower 330X
Main board (STM32-based)
GUI board (STM32-based) Includes buttons/display
Wire Sensor
Wire Sensor
Wire Sensor
Collision Sensor
Collision Sensor
Accel
Research/ROS (Target Computer)
Serial port
am_driver
IMU
(9150)
am_mpu9150
Serial port
roscore
”magic ros node”
Magic
sensor
”magic ros node”
”magic ros node”
”Standard Mower SW”
With special research mode.
Wheel Motor
Wheel Motor
Encoder
Encoder
GPS*
WIFI HW (Access Point)
Host Computer (Ubuntu + ROS)
Battery
* Not exposed to ROS

## Slide 6: HRP Driver Package Descriptions
am_driver
Description: Interface to the Automower via serial port.
Published topics:
/odom - position of robot given encoder data
/loop - status of boundary loop sensors
/sensor_status - status of collision sensors
/wheel_encoder - ticks read from the automower
Subscribed topics:
/cmd_vel - speed to assign to mower (linear and angular) /cmd_mode - mode of control for mower
am_mpu9150
Description: Interface to the mpu9150 imu via i2c.
Published topics:
/imu - fused quaternion and raw data (no covariance)
/imu_euler - fused heading in +-pi
Subscribed topics: none

## Slide 7: Getting Started
Unpack delivery file into the source folder of a catkin workspace (tar -xvf [delivery file])
Build using catkin_make
Simulator:
  setup the model path: export GAZEBO_MODELPATH= [the source folder]/hrp/am_gazebo/models:GAZEBO_MODELPATH
  Launch simulator using roslaunch am_gazebo am_gazebo_vslam.launch gui:=true
  Launch keyboard control with rosrun am_control keyboard_teleop.py
  You can now hopfully drive around in the simulated garden in gazebo!
Target:
  unpack and build the delivered software on the target computer
  make sure that the serialPort and i2cbus defined in the launch file (am_driver/launch/automower_vslam.launch)match those on your target computer.
  Launch target with roslaunch am_driver automower_vslam.launch
  Tell host that ros master is on target by exporting correct ROS_IP, ROS_HOSTNAME and ROS_MASTER_URI
  Launch keyboard control on host with rosrun am_control keyboard_teleop.py

## Slide 8
www.husqvarnagroup.com