Husqvarna Research Platform – getting started

On robot:
- Change power switch to on
- Enter PIN code: 1111
- Press MENU
- Hold 7 and 9 until new menu (tools) appears
- Select the wrench and press OK
- Select “Special settings” (last entry in list), press OK
- Tick “Override loop detection” by pressing OK
- Press OK to confirm
- Press start, or back until start menu and then start.
- Close hatch (or press plastic switch), display should now say “MOWING” amd the platform is ready.

On computer:
- Install some additional packages:
  - sudo apt-get install ros-indigo-nmea-msgs libcgal-dev screen
- catkin _make workspace (might need to do rosdep install first)
- For using Gazebo / simulation
  - Export robot model path:
    - export GAZEBO_MODEL_PATH=<ws>/src/hrp/am_gazebo/models:$GAZEBO_MODEL_PATH
  - launch simulator (with GUI, if wanted. There are more parameters to test!)
    - roslaunch am_gazebo am_gazebo_hrp_tracking.launch gui:=true
- For using with platform
  - Check which tty the platform is connected (normally ttyACM0 ?)
    - dmesg | grep ACM
  - Add user to dialout group
    - sudo adduser <username> dialout
  - Log out and log in again (to update group)
  - Update device
    - screen /dev/ttyACM0 115200
    - kill screen (nothing will be visible until you press k)
      - ctrl+a, k, y
  - You can now run driver (don't forget to launch roscore)
    - rosrun am_driver am_driver_node
    - If everything works, you should have Serial port ONLINE!, Serial port connected!
  - Launch teleoperation node
    - rosrun am_control key_teleop.py

For running uwb sensor (beacons) – assuming it is connected to /dev/ttyyUSB0
- rosrun am_uwbrange am_uwbrange_node _serialPort:=/dev/ttyUSB0
- Information is published to topic /uwb